## Slide 1
Design of a sailplane with a semi-monocoque wing
I. Aerodynamics and stability
Senadheera H.W.M.L.U.C
230593A
1

## Slide 2
Requirements and constraints
  Wingspan (b) : 12m - 18m
  Fuselage length : 45-55% of the wingspan
  Mass of complete aircraft : 250kg - 300kg
  Maximize the range of the aircraft.
2

## Slide 3
Determining the initial parameters
AR = 24
Wing Span = 15m
Calculated paramters
Wing Area (S) = 9.375 m^2
Mean chord ( c ) = 0.625 m
Wing Loading = 29.333 kg/m^2
Design Weight = 275.000 kg (2697.75 N)
Cruise speed = 22.183 m/s (79.86 km/h)
3

## Slide 4
  E603
  FX66S196
  FX67K170
  FX73K170
  FX60126
  FX61184
  FXS02196
  GOE533
  GOE549
  NACA23012
  NACA636318
Airfoil Selection for Wing
4

## Slide 5
5

## Slide 6
6

## Slide 7
7

## Slide 8
8

## Slide 9
  FX67K170
  FX73K170
  FX60126
  FX61184
  GOE533
Airfoils Selected
9

## Slide 10
Decision Matrix
10

## Slide 11
11

## Slide 12
12

## Slide 13
13

## Slide 14
Recuired CL
Angle of attack of airfoil and wing
AoA of airfoil matched = 2.50 0
At 2.50 0
Cl = 0.8710
Cd = 0.00731
Cl/Cd = 119.15
Generated Lift (L) = 2701.27 N
Infinite wing (2D aerofoil) lift curve slope, 𝑎0
IFinite wing lift curve slope; 𝑎 :
Zero-Lift Alpha (alpha0): -5.80 deg
AoA of wing
14

## Slide 15
Using XFLR 5..
Angle of attack of wing =5 deg
15

## Slide 16
Taper Ratio
Prandtl’s Lifting-Line Theory (LLT)
16

## Slide 17
After adding the taper to the wing
17

## Slide 18
Taill design calculations
Wing Area = 9.375 m2
CL (required) = 0.8699
Horizontal tail volume = VH = 0.6
Tail area
Optimum Tail arm
Tail Aspect Ratio (AR) : 16.00
Calculated Tail Span(b): 4.5380 m
Calculated Tail Chord(c): 0.2836 m
18

## Slide 19
Airfoil selection for tail and AoA
Airfoil - NACA0012
Similarly as for the wing using polar values:
Required AoA of airfoil : -2.793°
Infinite wing (2D aerofoil) lift curve slope, 𝑎0 : 6.9828 /rad (0.1219 /degree)
IFinite wing lift curve slope; 𝑎 : : 6.1310 /rad(0.1070 /deg)
AOA of Tail = -2.9269 deg
19

## Slide 20
XFLR 5 model of wing and tail
20

## Slide 21
21

## Slide 22
From the CM vs alpha curve which is the resultant of the wing and the tail has the trim angle less a than 1 degree. Therefore , can consider as almost zero

## Slide 23
22

## Slide 24
Fuselage Selection
  For sailplanes the CD0 vary in a range of : 0.012 - 0.95
  Choosed an arbitatry value of CD0 = 0.2200
  Wing Profile Drag (CD0_wing) = 0.0120
Using the equation
CD = CD0 + CDi
the grad polar curve of aircraft is being plotted around the CL value generated.
At CL = 0.8944,
Induced Drag (CDi) : 0.011878
Total Drag (CD_total) : 0.231878
Fuselage Profile Drag (CD_fuselage) : 0.208000
  We have choose a fuselage shape that has this amount of profile drag coeffcient or less than that
23

## Slide 25
Different fuselage shapes and relevant profile drag coefficient
Selected fuselage shape
24
[1] A. Singh, “Designing Procedure for Micro-Class Remote Controlled Fixed Wing VTOL,” International Journal of Engineering Science and Computing (IJESC), vol. 9, no. 9, 2019.

## Slide 26
References
[1] A. Singh, “Designing Procedure for Micro-Class Remote Controlled Fixed Wing VTOL,” International Journal of Engineering Science and Computing (IJESC), vol. 9, no. 9, 2019.
[2] Flight Manual for Self-Launching Sailplane PIK-20, approved by the National Board of Aviation, Finland.
[3] Soaring Society of America, “Self-Launching Sport Sailplane Design Competition Award,” award certificate presented to H. Van Neermeulen, Virginia Polytechnic Institute and State University, Second Place, 1981–1982.
[4] M. H. Sadraey, Aircraft Design: A Systems Engineering Approach. Hoboken, NJ, USA: John Wiley & Sons, 2012.

## Slide 27
THANK YOU